## Slide 1: HAV Exposure Monitoring vs Measurement Herefordshire Health and Safety Group

## Slide 2
HAVS The Issue Section One | 03
HAV Risk Assessment Challenges Section Two | 05
HAV Exposure Management Section Three | 11
Reactec Approach Section Four | 13
In Summary Section Five | 16

## Slide 3
How likely are you to develop havs?
Established correlation between time to vascular damage (white finger) and average daily exposure
HAVS
CTS
2018 Industrial Disease RIDDORS

## Slide 4
How likely are you to develop havs?
10% of employees exposed at the exposure action level will contract HAVS within 12 years or within 6 years if exposed to the exposure limit level. (HSE)
“Exposure below the Action Value cannot be considered safe...” (HSE)
Dy, years | 4 | 8 | 12 | 15
A(8), m/s2 | 7 | 3.7 | 2.5 | 2.0
Daily Exposure Pts | 784 | 219 | 100 | 64
Established correlation between time to vascular damage (white finger) and average daily exposure

## Slide 5: Legal obligations
The Control of Vibration at Work Regulations 2005 and associated guidance requires the following;
Elimination or control of vibration exposure risk to As Low As Reasonably Practicable (ALARP).
An assessment of the risks to employees from exposure to vibration, including assessment of employees’ daily exposure to vibration.
Information, instruction and training to tool users and their managers.
A suitable and sufficient assessment of HAV exposure risk requires a determination of;
duration of exposure and;
probable vibration magnitude during exposure.

## Slide 6: Assessing HAV Exposure
Angle grinder
Vibration magnitude 5m/s2
Trigger time: 3 hours
150 EXPOSURE POINTS
*HSE Website: www.hse.gov.uk/vibration

## Slide 7
Why does HAVS still dominate RIDDORS?
Does the risk assessment match the real tool use
How representative is vibration data used for risk assessments
Inadequate or ineffective controls.
Operator competency
01
02
03
04
05
Is the right tool being used for the job

## Slide 8
Condition of tool
Condition of tool accessory
Operator competency
Material being worked
30
25
20
15
10
5
0
Vibration Magnitude (m/s2)
Impact drill
rock drill
Chipping hammer A
Key
Range of vibration in intended use
declared
emission
mean vibration in intended use
01
02
03
04

## Slide 9
Drills Imact: Can give very high vibrations if operators push too hard. Maintaining sharp drill bits is important.
Angle grinders: Vibration values will depend on force being applied and different materials being worked. Selecting the right grade of abrasive and applying the right forces can help to minimise exposures.
Impact wrench: Measured vibration levels are dependent upon rates of use. It can be difficult to assess exposure times correctly.
Orbital sander: Vibration magnitudes are very dependent upon applied force. Lower vibration magnitudes can be achieved by applying the correct forces and using the appropriate abrasives.
Reciprocating saw: Operator training and work organisation is important. Lower vibrations can be achieved by keeping the tool’s nose against the workpiece.
Linishing: Vibration magnitudes vary greatly with applied force and condition of linishing belt.
7 to 13m/s2
7 to 11m/s2
3 to 10m/s2
4 to 12m/s2
7 to 27m/s2
HSE Appendix 3

## Slide 10
Even with the right training, it’s hard to know just how closely everyone is following health and safety protocols. Individuals taking more risk than you want, and unchecked exposure could damage your organisaton down the line.
Immediate and long-term gains require a shift towards prevention rather than simply compliance. Measure what’s happening, tailor your controls faster, engineer out risk and actively protect your workers health in the workplace.
Chart: HAV Exposure
| Joe | Jim | Dave | Les | Mike | Pete | Brian | John | Fred | Si | Bill | Greg | George | Dan
Max in one excavation | 64.1965 | 158.7244 | 251.1777 | 56.1456 | 224.1059 | 371.5177 | 118.8591 | 107.8019 | 74.4916 | 129.8958 | 37.857 | 137.4995 | 254.5792 | 47.0596
How good are your risk assessments?

## Slide 11
A grip mounted vibration magnitude measurement which can be compliant to ISO5349...

… will not be suitable for monitoring HAV exposure all day from multiple tool use.
X
Measurement
Can be suitable for monitoring HAV exposure all day from multiple tool use and assess exposure as required by “The Control of Vibrations at Work Regulations 2005”.
A wrist or tool mounted HAV monitor* does not measure in full compliance to ISO5349.

X
Assessment / Monitoring
Approximately right or exactly wrong

## Slide 12
Risk assessment should be a continuous process
PLAN
Plan Initial Risk Assessment
1
2
3
4
DO
Monitor Exposure Levels
CHECK
Review controls effectiveness
ACT
Improve controls & revise risk assessments
PLAN, DO, CHECK, ACT Management method for the control & continuous improvement of risk
Initial risk assessments of employees exposed to vibration are required to establish an appropriate set of controls and determine if occupational health screening is required.
Monitoring can help validate risk assessments.
Tool mounted and wearable on the wrist devices can be used to monitor HAV exposure.
Review the performance of controls and identify improvements to reduce risk ALARP.
Are monitored risk levels in keeping with initial assessment
Have control measures resulted in risk levels desired

## Slide 13: HAVS prevention
HAVWEAR is a wearable device giving unique insight into individual exposure levels to Hand Arm Vibration and personal alarms to directly influence behaviour.
More powerfully, combining the HAVWEAR with automatic data capture to the rich environment of the Reactec Analytics, all levels of management have enabling information to effectively manage the HAV exposure of their workforce at their finger tips

## Slide 14
Pre-determined expected vibration magnitude
2
Trigger time of Tool Use
Real use sensed vibration magnitude
2
Trigger time of Tool Use
Tool Exposure Points (TEP)
COMPLIANT with HSE Guidance
Sensed Exposure Points (SEP)
Independently validated by the IOM
=
=
x
x
HAVWEAR
2 Concurrent Assessments

## Slide 15
Reactec Credentials
Clients +900
Employees protected +75,000
Tool records +20M
Software users +9,000

## Slide 16: In Summary
HAVS damage is irreversible with a latency which can lead to complacency. However HAVS is preventable.
HAV risk assessments are a legal requirement
Risk assessments do not require precision measurements
They do need to be representative enough to implement effective controls
01
02
03